## Slide 1
Smart Agriculture system for precision Farming
Team Guide:
V. Nirmala
Team Members:
P.Chanikya – 321129512048
A.Anil kumar reddy - 321129512002
P.Akhil kumar - 321129512047
k.Mahesh - 321129512031

## Slide 2
Abstract
Weather API Integration: Fetches live weather data (e.g., temperature, humidity, pressure, wind speed, weather condition) from OpenWeatherMap API to predict weather patterns like rainfall or dryness.
Real-Time Environmental Monitoring:
Uses DHT22 sensor to measure temperature and humidity.
Employs three soil moisture sensors to monitor different soil zones and calculates an average moisture value for accuracy.
Smart Irrigation Decision System:
Sends weather and soil data to a Groq AI-based model.
Based on AI response, the system automatically controls a relay module to start or stop irrigation.
Manual & Auto Control Modes:
Auto mode: Fully controlled by AI predictions.
Manual mode: User can override AI decisions via a web dashboard or mobile app to control the motor manually.
Firebase Realtime Database:
Stores all sensor values (temperature, humidity, soil moisture, etc.).
Maintains current mode status (auto/manual) and relay (motor) status.
Twilio SMS Alerts:
Sends important updates like irrigation ON/OFF, low moisture warnings, and weather alerts to farmers using Twilio API.
Helps farmers stay informed even without internet access.
Sustainable Farming Approach:
Reduces water wastage by intelligent irrigation.
Aims to improve yield and optimize resource usage efficiently.

## Slide 3
Importance of Agriculture
Agriculture is the backbone of most economies, especially in developing countries like India, where over 50% of the population depends on farming for livelihood.
It provides the primary source of food, raw materials, and employment to a large portion of the population.
Agriculture contributes significantly to GDP, exports, and ensures food security for the nation.
It supports various allied industries like textiles, food processing, and pharmaceuticals.
With a rising global population, sustainable and efficient agricultural practices are critical to feeding the world.
Challenges Faced by Farmers
Water Scarcity
  Irrigation is often inefficient, leading to water wastage.
  Over 70% of available freshwater is used in agriculture, yet many farmers face unpredictable rainfall and dry spells.
Climate Unpredictability:
  Sudden weather changes like droughts, floods, and unseasonal rains impact crop yield.
  Farmers lack accurate, real-time weather forecasting tools to make informed decisions.
Low Productivity:
  Due to outdated farming methods and lack of access to modern technology.
Lack of Real-time Information:
  Farmers do not receive timely updates on soil condition, weather, or irrigation needs.
  Leads to either over-irrigation or under-irrigation, affecting crop health.
Manual Monitoring:
  Traditional methods require constant physical presence in the field, making it labor-intensive.

## Slide 4
Automate Irrigation
Design an intelligent irrigation system that uses real-time sensor data and AI-based decision-making to automatically control water flow.
Reduce the need for manual monitoring and operation of irrigation systems.
Improve timing and accuracy of irrigation to match actual crop needs.
Optimize Water Usage
Ensure water is supplied only when necessary, based on soil moisture levels and weather predictions.
Prevent over-irrigation and under-irrigation, thus conserving water and protecting crops.
Enable precision farming that uses just the right amount of water at the right time, promoting sustainable agriculture.
Notify Farmers with Real-Time Decisions
Use Twilio API to send automated SMS alerts to farmers when:
  Irrigation is turned ON or OFF
  Soil moisture drops below critical level
  Rain is predicted soon (to prevent unnecessary watering)
Objective

## Slide 5
Scope of the Project
Supports AI-Based Decision Making
Leverages machine learning models via Groq AI to make intelligent irrigation decisions, reducing human errors and increasing efficiency.
Sustainable Agriculture Focus
Promotes eco-friendly practices by conserving water and reducing dependency on traditional guesswork-based irrigation methods.
Future Integration Possibilities
Can be extended with:
Solar power modules for remote operation
Crop health image recognition via ESP32-CAM
Fertilizer scheduling based on soil condition
Wide Crop Compatibility
The system can be adapted for a variety of crops including paddy, wheat, vegetables, and horticultural plants by tuning irrigation thresholds and AI logic.

## Slide 6
Hardware Components
Soil moister sensor
ESP32
DHT22 sensor
Relay module
Motor pump

## Slide 7
Sensors Working
DHT22 (Temperature & Humidity Sensor)
Measures ambient temperature and humidity.
Uses a digital signal to send data to ESP32.
Helps monitor weather conditions affecting crop growth.
Soil Moisture Sensor
Measures volumetric water content in the soil.
Outputs analog voltage based on moisture level:
  Dry soil = low value,
  Wet soil = high value.
Three sensors are used, and the average is taken for accurate analysis.
ESP32 Microcontroller
Central unit that collects sensor data and controls the system.
Connects to Wi-Fi, communicates with Firebase, Groq AI, and Twilio.
Makes decisions and switches relay ON/OFF accordingly.
Relay Module
Acts as a switching device to control the motor (pump).
Triggered by ESP32 using a LOW signal (active LOW).
Isolates low-voltage control side from high-voltage motor side.
Water Pump (Motor)
Operates based on relay status.
Turns ON when soil moisture is low and AI allows irrigation.
Turns OFF automatically or manually through app or dashboard.

## Slide 8
System Architecture Overview

## Slide 9
Software Components
Arduino IDE
Used to code and upload programs to ESP32.
Supports sensor libraries and serial debugging.
Firebase Realtime Database
Stores sensor data and system states (mode, relay).
Enables real-time sync between ESP32 and app.
HTTP protocal
Acts as a local API to connect ESP32 with Groq AI.
Sends data, receives irrigation decisions.
Groq AI API
Analyzes weather + soil data for smart irrigation.
Provides AI-based decisions to control motor.
Twilio API
Sends SMS alerts to farmers.
Notifies about irrigation and weather updates.
Kodular App
Android app to control and monitor the system.
Supports manual/auto mode and shows live data.

## Slide 10
OpenWeatherMap API Integration
The ESP32 fetches real-time weather data from the OpenWeatherMap API over Wi-Fi using HTTP requests.
The data helps the system make climate-aware irrigation decisions by predicting rain or detecting harsh environmental conditions.
Weather Data Acquisition – OpenWeatherMap API
Parameter | Description
TempMax | Maximum forecasted temperature (°C)
Temperature | Current ambient temperature (°C)
Humidity | Atmospheric humidity (%)
Pressure | Atmospheric pressure (hPa)
WindSpeed | Wind speed (m/s or km/h)
Description | General weather condition (e.g., sunny, cloudy)
Parameters that are used as input to the Groq AI API to decide whether irrigation is required.
Sample JSON Format
{
"TempMax": 35,
"Temperature": 28.4,
"Humidity": 65,
"Pressure": 1012,
"WindSpeed": 10,
"Description": "partly cloudy"
}
Sea level | Atmospheric pressure at sea level | 
Grnd level | Atmospheric pressure at ground level

## Slide 11
Sensor & Weather Data Sent ESP32 sends soil moisture and weather data (temperature, humidity, rain forecast, etc.) to a http protocal .Groq AI Integration The HTTP protocal forwards this data to the Groq AI API, which processes the information using a trained model.
Decision Logic The AI evaluates:
Soil moisture levels
Rain possibility
Weather conditions
Irrigation Decision Based on the AI analysis, it sends back a decision like: “Irrigation Required” or “No Irrigation Needed”.
Action Trigger If irrigation is required and system is in auto mode, ESP32 activates the relay to turn ON the motor.
AI Decision Making (Groq AI)

## Slide 12
Decision Flow Diagram
ESP32
MICRO CONTROLER
Soil moister sensor
DHT22
Weather API
GROQ Ai
Firebase
RELAY
APP
R/W data
HTTP protocol
ON/OFF
TWILIO
Send command
Weather data
Moister values
Temp & hum
R/W data

## Slide 13
Auto vs Manual Control
Firebase-Based Control
A control flag (mode) is stored in the Firebase Realtime Database as either:
  “auto” → AI-driven control
  "manual" → User control via dashboard
Auto Mode (AI-Controlled)
System uses Groq AI decisions based on:
  Soil moisture
  Weather forecast
If irrigation is needed, relay turns ON automatically.
Ideal for hands-free operation in smart farming.
Manual Mode (User-Controlled)
Farmers can manually turn ON/OFF the motor via:
  Web dashboard
  Mobile app (Kodular)
Useful when the farmer wants to override AI decisions
Auto mode
Manual mode
This dual-mode feature ensures flexibility, safety, and trust, allowing farmers to switch based on their comfort or emergency situations.

## Slide 14
Firebase Database Structure
Explanation of Keys:
mode: Current operation mode (auto or manual)
relayStatus: Reflects the motor state (ON or OFF)
sensors: Real-time values from DHT22 and soil moisture sensors
weather: Weather data from OpenWeatherMap API
aiDecision: Latest AI prediction from Groq

## Slide 15
User Interaction & Communication
Kodular App Interface
User-friendly mobile app created using Kodular
Displays real-time sensor data (temperature, humidity, soil moisture)
Allows farmers to manually control the motor (ON/OFF)

## Slide 16
Twilio SMS Alerts
Real-Time Irrigation Notifications
System sends automated SMS alerts to the farmer's mobile using the Twilio API.
When are SMS Alerts Triggered?
When AI (Groq) predicts irrigation is required
When soil moisture is too low and auto mode is active
When manual control is activated via app
Why Twilio?
Works even in remote areas without mobile apps or internet
Ensures farmer awareness and trust in automation
Twilio adds reliability and accessibility by keeping the farmer informed of important actions taken by the smart agriculture system.

## Slide 17
Testing Setup

## Slide 18
#include <WiFi.h>#include <HTTPClient.h>#include <ArduinoJson.h>#include <mbedtls/base64.h>#include <DHT.h>// Firebase#include <Firebase_ESP_Client.h>#include <addons/TokenHelper.h>#include <addons/RTDBHelper.h>// Wi-Fi Credentialsconst char* ssid = "ppurnamma";const char* password = "17861787";// OpenWeatherMapconst char* weatherApiKey = "06ea9d51a37babf63dcf0f165ea8f592";const char* weatherBaseUrl = "https://api.openweathermap.org/data/2.5/weather";// Groq AIconst char* groqApiKey = "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";const char* groqApiUrl = "https://api.groq.com/openai/v1/chat/completions";// Twilioconst char* twilioSID = "AC73a915c2b4244700612c37a98ba1761d";const char* twilioAuthToken = "2432a6275a42d200232df920a297489a";const char* twilioFrom = "+12706068368";const char* twilioTo = "+919398612747";// Firebase#define API_KEY "AIzaSyC7lhw3aFo_iINX440iYnho05_xdvLisXo"#define DATABASE_URL "https://esp32-rtdb-30f4a-default-rtdb.firebaseio.com/"#define USER_EMAIL "charanponnada1787@gmail.com"#define USER_PASSWORD "charan@1787P"// Locationfloat lat = 12.9716;float lon = 77.5946;// Sensor Pins#define SOIL_SENSOR_1 34#define SOIL_SENSOR_2 35#define SOIL_SENSOR_3 32#define RELAY_PIN 27#define DHTPIN 21#define DHTTYPE DHT22// Globalsfloat availableMoisture = 0.0;float requiredMoisture = 450.0;float temperature = 0.0;int humidityValue = 0;// Firebase objectsFirebaseData fbdo;FirebaseAuth auth;FirebaseConfig config
;// DHT objectDHT dht(DHTPIN, DHTTYPE);void setup() { Serial.begin(115200); pinMode(RELAY_PIN, OUTPUT); digitalWrite(RELAY_PIN, LOW); // Default OFF dht.begin(); WiFi.begin(ssid, password); Serial.print("Connecting to Wi-Fi"); while (WiFi.status() != WL_CONNECTED) { delay(500); Serial.print("."); } Serial.println("\nConnected to Wi-Fi"); // Firebase setup config.api_key = API_KEY; config.database_url = DATABASE_URL; auth.user.email = USER_EMAIL; auth.user.password = USER_PASSWORD; Firebase.begin(&config, &auth); Firebase.reconnectWiFi(true); while (auth.token.uid == "") { Serial.print("."); delay(500); } Serial.println("\nFirebase is ready!"); fetchSensorData(); // Initial read}void loop() { delay(60000); // Every 1 minute fetchSensorData();}void fetchSensorData() { int s1 = 4095 - analogRead(SOIL_SENSOR_1); int s2 = 4095 - analogRead(SOIL_SENSOR_2); int s3 = 4095 - analogRead(SOIL_SENSOR_3); availableMoisture = (s1 + s2 + s3) / 3.0; temperature = dht.readTemperature(); humidityValue = dht.readHumidity(); if (isnan(temperature) || isnan(humidityValue)) { Serial.println("Failed to read from DHT22!"); return; } Serial.printf("Moisture: %.2f | Temp: %.2f°C | Humidity: %d%%\n", availableMoisture, temperature, humidityValue); // Upload to Firebase String path = "/ESP32/sensors"; Firebase.RTDB.setFloat(&fbdo, path + "/temperature", temperature); Firebase.RTDB.setFloat(&fbdo, path + "/humidity", humidityValue); Firebase.RTDB.setFloat(&fbdo, path + "/soil_moisture", availableMoisture); Firebase.RTDB.setInt(&fbdo, path + "/soil1", s1); Firebase.RTDB.setInt(&fbdo, path + "/soil2", s2); Firebase.RTDB.setInt(&fbdo, path + "/soil3", s3); checkModeAndControl();}void checkModeAndControl() { if (Firebase.RTDB.getString(&fbdo, "/ESP32/mode")) { String mode = fbdo.stringData(); // Clean unwanted characters mode.trim(); // Removes leading/trailing whitespace mode.replace("\"", ""); // Remove double quotes mode.replace("\\", ""); // Remove backslashes Serial.println("Mode: " + mode); // Clean output: Mode: manual / Mode: auto if (mode == "manual") { if (Firebase.RTDB.getString(&fbdo, "/ESP32/relayStatus")) { String relayState = fbdo.stringData();
codes

## Slide 19
// Clean relayState as well relayState.trim(); relayState.replace("\"", ""); relayState.replace("\\", ""); if (relayState == "ON") { digitalWrite(RELAY_PIN, HIGH); Serial.println("Manual Mode: Relay ON"); } else { digitalWrite(RELAY_PIN, LOW); Serial.println("Manual Mode: Relay OFF"); } } return; // ✅ Exit here to skip AI control } } // If not manual, go to AI logic fetchWeatherData();}void fetchWeatherData() { HTTPClient http; String url = String(weatherBaseUrl) + "?lat=" + String(lat) + "&lon=" + String(lon) + "&appid=" + String(weatherApiKey) + "&units=metric"; http.begin(url); int httpCode = http.GET(); if (httpCode > 0) { String response = http.getString(); Serial.println("Weather Response:"); Serial.println(response); DynamicJsonDocument doc(2048); deserializeJson(doc, response); String description = doc["weather"][0]["description"].as<String>(); String prompt = "{ \"temperature\": " + String(temperature) + ", \"humidity\": " + String(humidityValue) + ", \"weather\": \"" + description + "\", \"available_moisture\": " + String(availableMoisture) + ", \"required_moisture\": " + String(requiredMoisture) + " }"; analyzeWithGroq(prompt); } else { Serial.printf("Weather API Error: %s\n", http.errorToString(httpCode).c_str()); } http.end();}void analyzeWithGroq(String data) { HTTPClient http; http.begin(groqApiUrl); http.addHeader("Content-Type", "application/json"); http.addHeader("Authorization", "Bearer " + String(groqApiKey)); DynamicJsonDocument req(2048); req["model"] = "llama-3.3-70b-versatile"; JsonArray messages = req.createNestedArray("messages"); // Add system message JsonObject systemMessage = messages.createNestedObject(); systemMessage["role"] = "system"; systemMessage["content"] = "Analyze the weather and moisture data. Reply ONLY with 'Water Required' or 'Water Not Required'."; // Add user message JsonObject userMessage = messages.createNestedObject(); userMessage["role"] = "user"; userMessage["content"] = data; String requestBody; serializeJson(req, requestBody); int code = http.POST(requestBody); if (code > 0) { String response = http.getString(); Serial.println("Groq Response:"); Serial.println(response); DynamicJsonDocument res(2048); deserializeJson(res, response); String decision = res["choices"][0]["message"]["content"].as<String>(); sendSMS(decision); } else { Serial.printf("Groq API Error: %s\n", http.errorToString(code).c_str()); } http.end();}String base64Encode(const String& input) { size_t outputLen; unsigned char encoded[1024]; mbedtls_base64_encode(encoded, sizeof(encoded), &outputLen, (const unsigned char*)input.c_str(), input.length()); return String((char*)encoded);}
void sendSMS(String decision) { if (decision.indexOf("Water Required") >= 0) { digitalWrite(RELAY_PIN, HIGH); Serial.println("AI Decision: Watering ON"); } else { digitalWrite(RELAY_PIN, LOW); Serial.println("AI Decision: Watering OFF"); } // --- Twilio SMS --- HTTPClient http; String msg = "Temp: " + String(temperature) + "°C, Humidity: " + String(humidityValue) + "%, Moisture: " + String(availableMoisture) + ", AI: " + decision; String auth = base64Encode(String(twilioSID) + ":" + String(twilioAuthToken)); http.begin("https://api.twilio.com/2010-04-01/Accounts/" + String(twilioSID) + "/Messages.json"); http.addHeader("Authorization", "Basic " + auth); http.addHeader("Content-Type", "application/x-www-form-urlencoded"); String body = "From=" + String(twilioFrom) + "&To=" + String(twilioTo) + "&Body=" + msg; int httpCode = http.POST(body); if (httpCode > 0) { Serial.println("SMS sent successfully!"); } else { Serial.printf("SMS sending failed: %s\n", http.errorToString(httpCode).c_str()); } http.end(); // Log to Firebase Firebase.RTDB.setString(&fbdo, "/ESP32/relayStatus", decision); Firebase.RTDB.setString(&fbdo, "/ESP32/relayStatus", digitalRead(RELAY_PIN) == HIGH ? "ON" : "OFF");}

## Slide 20
Results

## Slide 21
Conclusion
This project showcases an AI-powered Smart Agriculture System that enhances irrigation efficiency and crop productivity.
By combining real-time sensor data, weather forecasting, and AI decision-making, the system ensures intelligent water management.
Features like auto/manual control, Firebase synchronization, Twilio SMS alerts, and a user-friendly dashboard/app make it accessible and practical for farmers.
The solution promotes sustainable agriculture, reduces water wastage, and empowers farmers with timely insights and control.

## Slide 22
Thank you